## Slide 1: CG1112
Week 5 – Studio 1
Timer (tick tock tick tock)

## Slide 2: Please take 5 minutes to register for your project group
Go to LumiNUS.
Click “Class and Groups” on the left bar, then “Class Groups” on the top bar. Click “B01” or “B02” etc.

## Slide 3: Please take 5 minutes to register for your project group
Choose your respective project group according to the map on the next page and sign up.
  If you are in Section 1 on the A side, your group is 1 B0x-1A (where x is your studio number. E.g. B03-1A)
  You may swap sides within a section. E.g. 1A->1B or 1B->1A
  Maximum of 5 persons in a group. Do not sign up for the wrong group.
  You are not allowed to join a group in a different section. E.g. if you are in Section 2, you cannot join group 3A.

## Slide 5: Oh, OC0A is PD6, which is Pin 6??

## Slide 6: OC0A interaction with PD6
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
PORTD |  |  |  |  |  |  |  | 

## Slide 7
Frequency 🡺 Duration
Clear Timer on Compare (CTC)
Prescaler

## Slide 8
TCCRnA | CmA1 | CmA0 | CmB1 | CmB0 | 3 | 2 | WGM1 | WGM0
TCCRnB | 7 | 6 | 5 | 4 | WGM2 | CSn2 | CSn1 | CSn0
OCRnx (8 bit)
TCNTn (8 bit)
WGM13 | WGM12 | WGM11 | WGM10 | Mode | TOP
0 | 1 | 0 | 0 | CTC | OCR1A
TCCR1A | CmA1 | CmA0 | CmB1 | CmB0 | 3 | 2 | WGM11 | WGM10
TCCR1B | 7 | 6 | 5 | WGM13 | WGM12 | CS12 | CS11 | CS10
OCR1A (16 bit)
TCNT1 (16 bit)
CSn2 | CSn1 | CSn0 | Description
0 | 0 | 0 | Stop
0 | 0 | 1 | clkIO / 1
0 | 1 | 0 | clkIO / 8
0 | 1 | 1 | clkIO / 64
1 | 0 | 0 | clkIO / 256
1 | 0 | 1 | clkIO / 1024
TC0 and TC2
TC1 only
TIMSKn | 7 | 6 | 5 | 4 | 3 | 2:OCIEB | 1:OCIEA | 0
cli() sei()

## Slide 9: Recommended Steps for SetupTimer()
cli(); //Disable all interrupt
TCCRnA = ......;
TCCRnB = 0; //Clear CS bits initialized by Arduino
TIMSKn = ......; //If Timer Interrupt is used
TCNTn = 0;
OCRnA = ......;
sei(); //Enable all interrupt

## Slide 10: ERRATA
Page 4 Question 5 Step 3:
“Locate the following segment of code in the w6s2p1 w5s1p1 sketch”
Page 5 Activity 2:
“Create a new Load the Arduino sketch called w5s1p2”